## Slide 1: 存储产品的测试

## Slide 2: 存储产品的测试 – 测试内容
单元测试：往往不由测试部门来做，而是开发者自己在开发过程中就完成。
功能测试：单个组件或单个功能的测试。
集成测试和系统测试：
  多个组件集成在一起，对组件间的接口部位进行测试。
  所有组件和功能集成在一起，形成产品。对整个产品进行测试。
  存储产品和其他产品混合使用，例如主机，交换机，数据库等。对整个环境进行测试，也是系统集成测试。
  特殊客户的特殊环境。偶尔可以对大客户环境进行有针对性地集中测试。

## Slide 3: 存储产品的测试 – 测试类型
Categories | Focal Point | Scenarios | Functional | Pass Criteria
Function / Regression | Normal use of designed functions. | MBT | YES | Product does exactly what it’s supposed to do. New functions don’t break existing functions.
CCT | Designed functions in typical customer configurations or large scale configurations. | Simulation of customer environment. | YES | Product performs correctly in customer environment.
Longevity | Longest survive time. | Categorized functions and CCT. | NO | Product lasts as long time as expected. No memory leak, no counter overflow.
Performance | Throughput and response time. | Comparison between performance goals and baselines. | NO | Performance goals are reached.
Stress | How software responds to peak load. | Overload the application on purpose until it breaks by applying both realistic and unrealistic load scenarios. | NO | Find the failure point of your piece of software.
Destructive | Misuse of software and normal use of software in skewed environment. | FMEA | MIX | No DL No Crash No Core dump No Hung Automatic Recovery Automatic Resuming

## Slide 4: 存储产品的测试 – 方法和工具
功能测试：
  方法：MBT ( Model Based Testing )
  工具/技术：FlowChart, EquivClass, BVA
  自动化：RF
系统集成测试
  方法：MBT, FMEA ( Failure Mode Effect Analysis )
  工具/技术： Customer Environment Analysis, FMEA Library，Workload Simulation，Fault Injection,
  自动化：WIDGET + CCTF
策略： Pairwise, Orthogonal Array

## Slide 5: 存储产品的测试 – MBT功能测试
MBT – Model Based Testing
基于需求（SR）对软件行为建模
在输入中可以应用各种测试技术如Equivalence Class, BVA等
在用例选择上可以利用各种策略如Pairwise, Orthogonal Table等
用例可以早于代码生成
自动化工具可以自动应用测试策略生成精简用例列表
例子：自动售货机

## Slide 6: 可靠性测试 – FMEA
SEV = How severe is effect on the customer? |  |  |  |  |  |  |  |  | 
OCC = How frequent is the cause likely to occur? |  |  |  |  |  |  |  |  | 
DET = How probable is detection of cause? |  |  |  |  |  |  |  |  | 
RPN = Risk priority number in order to rank concerns; calculated as SEV x OCC x DET |  |  |  |  |  |  |  |  | 
Process step | Potential failure mode | Potential failure effects | SEV | Potential causes | OCC | Current process controls | DET | RPN | Expected Response
What is the step? | In what ways can the step go wrong? | What is the impact on the customer if the failure mode is not prevented or corrected? | 10 | What causes the step to go wrong? (i.e., How could the failure mode occur?) | 10 | What are the existing controls that either prevent the failure mode from occurring or detect it should it occur? | 10 | 1000 | How is the software designed to respond to this failure?
 |  |  |  |  |  |  |  | 0 | 

## Slide 7: 测试资产 – FML（故障模式库）
ENTITY | MODULE | SUB MODULE | FAILURE MODE | CAUSES | SEV | OCC | DET | RPN
Where does the failure happen | what's the module | sub module | describe the failure | why failure happens | severity | occurance | detectable | risk priority number
SERVER |  |  | Whole Server Down | power issue, hardware broken, overheating | 10 | 1 | 1 | 10
HBA | Power | Regulator | Capacitor punchthrough | over voltage | 10 | 5 | 10 | 500
DISK | Sectors |  | Write error | Temperature, sector worn out | 10 | 10 | 10 | 1000
NETWORK SWITCH |  |  | Whole Switch Down | Power issue, hardware broken, overheating | 10 | 5 | 10 | 500
NETWORK SWITCH | Port |  | One port down | Hardware issue | 10 | 8 | 10 | 800

## Slide 8: 存储产品的测试 – 系统集成测试
我们要测试的内容并非单一的存储产品，而是整个数据中心!
  可能出现的各种软硬件的搭配组合
  可能发生的外部和内部事件
  可能出现的外部和内部故障
  可能出现的各种应用负载

## Slide 9: 数据中心案例: 某500强保险公司
寸土寸金的机房
  电气系统： UPS， 市电 + 工业电
  空调系统：精密空调 + 新风机
  消防系统：自动火灾报警系统、烟感设备、漏水报警系统、灭火系
  监控系统：7 * 24 录像， 门禁
  综合布线
  接地系统
  防雷系统
  装饰、防火隔断
  KVM 系统
  造价： 每平米 10000 RMB。（这还是10年前的水平。）
机柜系统：PDU，散热，KVM走线
服务器： IBM (AIX), HP (UX), SUN (Solaris), Intel x86_64 (Linux or Windows)
存储：SAN 网络 + 磁盘阵列
网络：核心交换机 + 子交换机
软件：性能监控、故障监控、虚拟化
业务系统：行业相关，但普遍采用虚拟化，数据库作为后端，中间件，以及廋客户端（例如浏览器），高可用群集软件做HA

## Slide 10: CCTF & WIDGETS
通用的可靠性测试框架

## Slide 11: Widget Framework
负载模拟 故障注入

## Slide 12: WIDGET FRAMEWORK - 业务负载+故障注入
  Widget Framework
  如何注入故障和模拟资源抢占？
  客户环境千变万化，如何灵活设计工具用以模拟客户应用？
  如何才能与测试框架无缝集成？

## Slide 13: 单个应用程序
APPLICATION
CPU 25%
MEM 70%
OPEN FILE 3
APPLICATION:
Combination of CPU, MEMORY usage and IO loads and kernel resources.
+-*/…foo()…If…then…else…++…--…=…==
Syscalls
25% CPU
70% System Memory
3 Files opened ( kernel structure )

## Slide 14: 整个系统
CPU
MEMORY
KERNEL STRUCTURES
DISK
NETWORK
APP1
25%
10 MB/s
Random
OPEN PORT 22
OPEN FILES 6
APP2
5%
APP3
APP4

## Slide 15: Widgets – Workload Generators & Fault Injectors
SUT
A widget is
  A small C application
  A Work Load Generator or a Fault Injector
  Remotely start/terminate/monitor
  Integration with any PERL/PYTHON based cases
Each widget does only one thing, hundreds of billions combinations of widgets makes complex environments.
New widgets can be automatically discovered by widget framework.
CCTF calls PYTHON API to control widgets
CPU Consumer
MEMORY
Consumer
I/O Load
Generator
Fragmentation
Generator
Process
Generator
Port Holder
File Descriptor
Holder
CPU Consumer
MEMORY
Consumer
I/O Load
Generator
Fragmentation
Generator
Process
Generator
Port Holder
File Descriptor
Holder
Daemon
Dash Board
CLI
API
Driver Node
CCTF Case

## Slide 16: WIDGETS
CPU
MEMORY
KERNEL STRUCTURES
DISK
NETWORK
25%
10 MB/s
OPEN PORT 22
OPEN FILES 6
5%
CPU WIDGET
MEM WIDGET
WRITER
PORT HOLDER
FD HOLDER
APP1

## Slide 17: A typical structure of a widget
Thread #2
main()
{
  init_widget();
  //…
  //… any operation, any codes
  //…
  publish_widmsg(); // as needed
  // …
  //… any operation, any codes
  // …
  quit_widget();
}
Listen for new messages
Process new messages with message handler
loop

## Slide 18: Concurrency Control Test Framework
灵活的并发流程

## Slide 19: 存储产品的测试 – 系统集成测试
我们要测试的内容并非单一的存储产品，而是整个数据中心!
  可能出现的各种软硬件的搭配组合
  可能发生的外部和内部事件
  可能出现的外部和内部故障
  可能出现的各种应用负载

## Slide 20: CCTF - 可控的并发
  CCTF – Concurrency Control Test Framework
  根据可靠性测试的需求定制的测试框架。同时具有通用性和扩展性。
  多线程设计以应对并发性的要求。
  一条命令完成部署，对系统没有特殊依赖，只需一台Linux或者Mac主机就能运行
  不需要任何配置文件，简单易用，提升用户的体验。
  抽象的基础包，提供可扩展性。
  模块化功能。

## Slide 21
The model of CCTF is a simulation of manual work in real world.
Any connectable thing is a “Target”. ( Host, Array controller, Switches, Routers etc … even a mobile phone can be a target if necessary )
Each target has one or more “Operators” working on it.
Each operator holds it’s own connection to the target and issues it’s own commands. Operators performs like individuals.
Operators perform concurrently.
A “Case” is the brain of operators, it’s like a commander, it assigns tasks to operators and get reports from operators.
The Case controls whole workflow, it tells operators what to do and wait for results, then decides either to fail or pass this scenario.
CCTF – Concurrency Control Test Framework

## Slide 22: CCTF Objects

## Slide 23
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
Driver Node
SUT
SUT
SUT
SSH/RSH/TELNET Connection
Monitor/Execute commands in Q
The case pushes commands in Q
Exposes a shell to user. Just Like an operator sitting in front of a console
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
This whole thing is an internal object - “shell object” in a CCTF case
A “shell” object holds a connection to an SUT, runs a private thread to execute commands and maintains a private command Q
Commands are issued from Driver Node to SUT through this Connection
A Private Command Q
A Private Thread
A Shell of SUT
An object
User can create multiple connections to an SUT - As many “shell” objects as it requires.
Shell.exe() – Push a command in Q without blocking main thread of a case
CCTF – Concurrency Control Test Framework

## Slide 24
Base Package
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
Driver Node
SUT
SUT
SUT
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
Driver Node
SUT
SUT
SUT
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
SSH/RSH/TELNET Connection
Product Package
Shell
bdoperator
Bdoperator1.2
Bdoperator1.0
Bdoperator1.1
Logic
Unit
Case
Unit
Widget API Package
widcpuloadgen
widmemloadgen
widfragmentgen
widwriter
widfileoper
widportholder
widprocessgen
widget
User Defined Case Unit
A case unit is a case fragment.
A case unit runs in a private thread.
User must write a child class of “Case Unit” and implement its virtual method.
A case unit is also an internal object of CCTF. It accepts parameters from the case.
Multiple case units can start together.
CCTF – Concurrency Control Test Framework

## Slide 25: CCTF – So, a CCTF case can be …
Straight Forward
Simple Concurrency
Case
Unit
Case
Unit
Case
Unit
Case
Unit
Start
End
Main Thread
Or, Mixed with
reusable case units

## Slide 26: Thanks! Q&A…
peng.chen@orcadt.com